### Suggested US Strategy for

### DCLL Blanket Tests in ITER

- Make optimum use of the unique features of ITER for testing key issues of the DCLL blanket concept in ITER:

- geometry of poloidal LM channels in a TBM identical to the one in a DEMO blanket module,

- magnetic field strength and –distribution identical in TBM and blanket module,

- relevant volumetric heating allowing to investigate natural convection in the large LM channels.

- Do not insist on investigations of limited values due to the inherent limitations in ITER:

- neutron flux too low to allow meaningful tests of the mechanical loading of the blanket structure,

- neutron fluence too low for the investigation of irradiation damages in the structural material,

- testing time and number of testing article too small for meaningful reliability tests.

- Concentrate on the key issues of the DCLL blanket concept:

  - Investigation of the liquid metal flow distribution and pressure drop in the strong magnetic field (MHD):

- multi-zone geometry (lead-lithium in the channels and in the gaps between insert and steel wall, FCI, helium-cooled steel walls),

- finite electrical resistance of the FCI’s,

- 3-D current flow in transition zones.

  - natural convection in the large channels and its impact on the temperature distribution in the Pb-Li and the channel walls,

  - Heat losses from the liquid metal breeder to the helium-cooled channel walls,

  - Conditions in the gaps between FCI and helium cooled walls.

- Suggested Strategy:

Try to come to an agreement with the EU to purchase the structure of the HCLL TBM including the following programmatic steps:

  - Design of the blanket box with the entire helium cooling system (TBM structure, helium manifolds, helium coolant access pipes, mechanical attachment of the TBM to the port frame),

  - Layout and analysis of the entire helium cooling system,

  - Stress analysis of the TBM structure and the attachment to the frame,

  - Transient electromagnetic testing of the TBM,

  - Neutronic tests of the TBM,

Main contribution of the US to the development and fabrication of DCLL TBM’s:

- Development and fabrication of flow channel inserts,

- Detailed pre-test analysis of the liquid metal flow in the TBM (MHD issues, heat losses to the helium cooled structure, velocity fields with inclusion of natural convection, pressure drops),

- Performance of the flow channel inserts under realistic conditions (electrical and thermal insulation, pressure equalisation, compatibility with lead-lithium).

- Instrumentation for the measurement of the LM flow conditions in the TBM under operating conditions,

- Extrapolation of the measured results to the conditions in a DEMO blanket.