## Slide 1: EU DEMO Project
Gianfranco Federici and the PPPT Team
Power Plant Physics and Technology

## Slide 2: Outline
Background/ Context
Design approach
Preliminary design choices
Main Design and R&D Priorities, e.g.:
  Power exhaust / divertor
  Tritium breeding / power extraction blanket
  Remote Maintenance
PPPT Implementation
Conclusions

## Slide 3: A roadmap to the realisation of fusion energy
  8 Strategic missions to address challenges in two main areas:
ITER Physics
  Risk mitigation for ITER
  JET, Medium Size Tokamaks, PFC devices
DEMO Design
  Conceptual design studies
  A single step to commercial fusion power plants
  Production of electricity with a closed fuel cycle
Back-up strategy
  Stellarator
Three periods (ITER on critical path/ schedule uncertainties)
2014 – 2020 (Building ITER & support experiments + DEMO CDA)
2021 – 2030 (Exploiting ITER and DEMO EDA)
2031 – 2050 (Building and Exploiting DEMO)
Important to increase the involvement of industry
PPPT Projects (total ~110 M€) 2014-18
EC contribution (~55%)

## Slide 4: Outstanding technical challenges with potentially large gaps beyond ITER
  ITER will show scientific/engineering feasibility:
  Plasma (Confinement/Burn, CD/Steady State, Disruption control, edge control)
  Plasma Support Systems (LTSC magnets, fuelling, H&CD systems)
  Most components inside the ITER VV are not DEMO relevant, e.g., materials, design. TBM provides important information, but limited scope.
Still a divergence of opinions on how to bridge the gaps to fusion power plants
Most of the issues are common to any next major facility after ITER
DEMO Issues/gaps
For any further step, safety, power exhaust, breeding, RH and plant availability are important design driver and CANNOT be compromised
T breeding blanket technology (M4)
Divertor design configuration and technology (M2 & M6)
Safety and licensing (M5)
  Plant design integration incl. BoP (M6)
  Operating plasma scenario and control and efficient CD systems (M1)
  Remote maintenance and plant availability (M6)

## Slide 5: Advanced Reactor Designs
Short Pulse…………………………….………………..Pulse Length………………………………..………………Steady State
Ceramic / LiPb Breeder / Eurofer…..…………..Blanket Technology……………………….…….LiPb / SiC/ DCLL
EUROFER <550C…………………………Max Temp. Structural Materials …………ODS RAFM/ HT FM> 600C
Conventional…..……………………………..…………..Divertor Configuration………………………Advanced Novel
LTSC Coils…………………………………….…….Magnet Technology….……………………………..HTSC with Joints
Decreasing Technology Readiness
Increasing Expected Performance








 = KPI Partially Met (DEMO 1)
 = KPI Fully Met
= Tech advancement needed to reach KPI targets (DEMO 1)
= Further Tech advance to fully reach KPI target (DEMO 2)
Safe Operation
T Self Sufficiency
Availability
Power Handling
Cost
Thermal Efficiency
Electrical Output
Departure from Existing Designs
Confirmation testing+ Engineering
Substantial R&D
Prototype and/or DEMO plant
+
Confirmatory testing
+
Engineering
Innovative designs,
i.e., design requiring substantial developments, GEN IV
Evolution thanks mainly to advances in safety, materials and technology (+ strong involvement of industry from beginning
Existing operating plants (high availability)
Evolutionary designs, GEN III
Costs of Development
(prior to commercial deployment)
ITER
(low availability)
Departure from Existing Designs (=ITER)
Development Paradigm: Fission Power Plants

## Slide 6: Basic Concept Design Approach
Define Requirements
Refine Design
Develop Design
Conduct R&D
Evaluate Design Performance
Decision Point:
develop further?
Design integration essential from the early stage to identify requirements for technology R&D
A systems engineering approach is needed to identify design trade-offs and constraints; and prioritize R&D
Ensuring that R&D is focussed on resolving critical uncertainties in a timely manner and that learning from R&D is used to responsively adapt the technology strategy is crucial.
Clear assessment methodology needed e.g., by assigning a TRL and updating TRL as R&D tasks are completed
Involvement of industry is highly desirable
Lessons learned from the pas

## Slide 7: Readiness of assumptions
Operational point (in terms of Beta N, q95, n/nGW, and H) should lie within the existing database of tokamak discharges that have run for at least several current redistribution times, implying that we also know how to control these scenarios.
Credible and sufficient power exhaust protection.
Adequate breeding coverage area.
Power transported by electrons and ions across separatrix:
  Psep=Pα+Padd-Prad,core
Material Limit Condition for divertor :
  Psep/R≤20MW/m  Psep,maxR
Boundary condition to access and stay in H-mode (PLHR):
  Psep ≥ PLH  Psep,minR
Divertor heat load and H-mode limits as a machine size driver
Psep/PLH
Psep/R
Prad,core/Prad,tot
PROCESS:
Fix Pel,net, pulse
Scan Zeff
R. Kemp (CCFE)

## Slide 8: EU DEMO design point studies
  Systems Code PROCESS to develop self-consistent design points.
      Rather than focusing solely on developing the details of a single design point keep some flexibility at the beginning
      Reasonable readiness of physics and technology assumptions
      Identify key driver and constraints (e.g., divertor protection, vertical stability)
      Sensitivity to design assumptions and impact of uncertainties [R. Kemp, IAEA/ FEC 2014 St. Petersburg] (e.g., Pulsed vs steady-state, A=R/a, TF Ripples, Divertor Protection)
  Iterate between the Systems Code and more detailed analysis such as integrated scenario modelling with transport codes (refine design space)
      Preliminary plasma scenario modelling [G. Giruzzi, IAEA/ FEC 2014 St. Petersburg]
      DEMO pedestal predictions [R. Wenninger, IAEA/ FEC 2014 St. Petersburg]
  This approach provides confidence in the choice of the operating point

## Slide 9: Preliminary DEMO design options being studied
Design features (near-term DEMO):
2000 MWth~500 Mwe
Pulses > 2 hrs
Single-null water cooled divertor
PFC armour: W
LTSC magnets Nb3Sn (grading),
Bmax conductor ~12 T (depends on A)
RAFM (EUROFER) as blanket structure
Vacuum Vessel made of AISI 316
Blanket vertical RH / divertor cassettes
Lifetime: starter blanket: 20 dpa (200 appm He); 2nd blanket 50 dpa 2nd, divertor: 5 dpa (Cu)
Open Choices:
Breeding blanket design concept selection planned for 2020
Primary Blanket Coolant/ BoP
Protection strategy first wall (e.g., limiters)
Advanced divertor configurations
Number of coils
 | Inductive (2.6) | Steady State
R0 / a (m) | 9.0/ 2.8 | 8.1/ 3
Κ95 / δ95 | 1.6/ 0.33 | 1.6/ 0.33
A (m2)/ Vol (m3) | 1687/ 3515 | 1318/ 2363
H-factor / BetaN | 1.1/ 2.8 | 1.3/ 3.4
Psep | 150 | 100
PF (MW) / PNET (MWe) | 2040/ 500 | 2104/ 500
Ip (MA) / fbs | 24/ 35% | 19.9/ 56%
B at R0 (T) | 4.2 | 5.0
Bmax conductor (T) | 9.8 | 12.2
BB i/b / o/b (m) | 1.07/ 1.56 | 
NWL MW/m2 | 0.9 | 1.2
Aspect ratio trade-off studies are underway
A=2.6
A=3.1
A=3.6
Under
revision

## Slide 10: Enabling DEMO Reactor Technologies
Readiness Now
Readiness after ITER
Water BoP (TRL 7-8)
Divertor RH
ECH 170 GHz
He BoP
(TRL 4-5)
Nb3Sn LTSC
(TRL 4)
NB (1MeV)
(TRL 3)
Blanket RH
(TRL 1-2)
Important experience relevant for DEMO is expected to be gained by the Construction, Commissioning and Operation of ITER.
Modest R&D, for some of the components, foreseen in Horizon 2020
Cryopumps
Nb3Sn LTSC
NB (1MeV)
Divertor RH
(TRL 7-8)
ECRH 170 GHz
(TRL 6-7)
Blanket RH
(TRL 4)
Diagnostics not fully relevant
(TRL 3 – 4)

## Slide 11: Divertor configuration and target R&D Strategy
Conventional divertors
Stability of detachment
ELMs and Disruptions
Sweeping/ Wobbling
Water cooled design
Armour: Tungsten
Structural: Cu-alloys
EOL <10 dpa, 200-350oC
Physics
Advanced divertors
Snowflakes
Super-X
Liquid Metals
Technology
Heat flows in a narrow radial layer (SOL) of width λq (~1 mm)
Scales only weakly with machine size [T. Eich 2013].
Forces on the PF coils are the critical issue
Plasma control problems
Design integration problems
Very LOW readiness
TRL
Limited effort on He-cooling and on LM
ITER
Single-null divertor
Water –cooled, 100oC (inlet)
W armour/ Cu-alloy as heat sink
Targets qualified for 20 MW/m2
DEMO
Notes: May 2014 HHF tests at IDTF in St Petersburg, beyond the design requirements
- 3 W mbs (2 ANSALDO 6 mm W and 1 Plansee 5.5 mm W)
- 5000 cycles at 10 MW/m2 + 300 cycles at 20 MW/m2 + 700 cycles at 20 MW/m2

## Slide 12: Encouraging recent results from Asdex-Upgrade
Divertor heatflux control with nitrogen seeding
Here: (weak) partial detachment
1/3 cryo, p0,div = 4 Pa
Room for stronger detachment?
 simpler and cheaper divertor !
Psep / R = 10 MW/m !
Psep/R is divertor identity parameter, provided similar density and power width q
A. Kallenbach, IAEA / FEC 2014

## Slide 13: DEMO breeding blanket: very low TRL No one is perfect!!!
Concerns | HCPB | HCLL | WCLL | DCLL
Tested in ITER TBM |  | ☺ |  | 
Suitability for Eurofer |  |  |  | 
FW heat flux capability |  |  |  | 
Safety issues of coolant |  |  |  | 
Technology readiness BoP |  |  |  | 
Potential for high coolant outlet temperature |  |  |  | 
Coolant pumping power |  |  |  | 
Shielding efficiency/ n-streaming void space |  |  |  | 
Activation products in coolant (water) |  |  |  | 
Breeding efficiency |  |  |  | 
Tritium extraction from breeder |  |  |  | 
Tritium extraction from coolant |  |  |  | 
Tritium permeation through heat exchanger |  |  |  | 
Tritium Breeding Blankets - the most important & novel parts of DEMO
Large knowledge gaps will exist even with a successful ITER TBM programme
Feasibility concerns and Performance uncertainties  Selection now is premature
Notes: Another equally challenging area is the Breeding Blankets, whose primary functions of:
Breeding sufficient Tritium to sustain fusion operations
Absorbing neutrons and extracting the thermal energy for use in electrical production
are really at the core of the DEMO Plant functionality.
Only HCPB and HCLL will be tested as part of the ITER TBM programme: but, even following a successful TBM prog, large knowledge gaps will remain due to the much lower n-fluence of ITER.
Here we can see a qualitative comparison of 4 breeding blanket concepts currently under assessment in the DEMO CDA phase. Clearly, each blanket concept has a mixture of strengths and weakness and much more R&D, design and analysis is required at both a system and component level in order to make an objective selection by 2020.

## Slide 14: EU Blanket Designand R&D Strategy (talk of L. Boccaccini)
Develop a feasible and integrated DEMO blanket system conceptual design of 4 concepts.
BoP cycle and technology plays a substantial role in concept selection.
Complementarity with TBM Programme

## Slide 15: Remote Maintenance Architecture Analysis
CAD models created:
Kinematic studies determine optimum design for maintenance
Vertical port maintenance preferred:
Simpler pipe handling
Ease of inboard segment extraction
Access to connection points for a crane
From a range of designs examined in 2011, options to 4 quasi-vertical alternatives went forward… ITER, Aries, NET, and free thinking alternatives
  Through the floor maintenance
Large upper port opening (NET)
Diverter on the roof
Straight vertical port
Courtesy of A. Loving and his team, CCFE
Vertical port maintenance preferred:

## Slide 16: Involvement of Industry
Areas of potential industrial involvement:
Technical Management
  Project / Programme Management
  Plant engineering processes: Systems Engineering and Design Integration
  Cost, risk, safety and RAMI analysis
  Evaluation and selection of design alternatives
  Plant engineering tools, modelling and simulation
  Technology assessment i.e. technology audits, TRL assessment, technology scenario analysis i.e. where are relevant technologies (e.g. HTS) going over the next 5 years?, etc.
Design Engineering
  Design for robustness and manufacture of critical components/systems; include design simplification/ reduce fabrication costs
  Impact assessment on the application of existing technologies under DEMO environmental / operating conditions i.e. pulsed operation on BoP components
  Manufacturing development and qualification with emphasis on performance and cost optimization of design solutions

## Slide 17: PPPT Implementation
A project-oriented structure set-up
Resources in Horizon 2020 secured
A new governance system based on the principle of joint programming

## Slide 18: PPPT Project Leaders
PPPT PMU
L. ZANI
Magnets
L. BOCCACCINI
Breeding Blanket
Containment
Structure
J. H. YOU
Divertor
A. LOVING
Remote Maintenance
W. BIEL
Diagnostics, Control
E. CIPOLLINI
Heat transfer, Balance
of Plant, Sites
C. DAY
Tritium, Fuelling
and Vacuum
M. Q. TRAN
Heating and
Current Drive
M. RIETH
Materials
Early Neutron
Source
N. TAYLOR
Safety and
Environment
Project control/
coordination
System & Design Integration
Physics Integration
Current Status of PPPT Projects:
Well defined scope of work / deliverables / milestones / resources
Interlinks /opportunities for industrial involvement + training
All PMPs approved by Project Boards

## Slide 19: PPPT PMU Team
BOTOND MESZAROS
Senior Configuration control and CAD management officer
Design integration
CAD management
?
Senior Breeding Blanket Project Control and Integration Officer
Blanket design integration
WPBB project RO
WPTFV project RO
RONALD WENNINGER
Physics Integration Group Manager
CLAUDIUS MORLOCK
Project Control Group Manager
CHRISTIAN BACHMANN
System Level Analysis and Project Coordination Officer
Design integration
System level analysis
WPDIV project RO
WPCS project RO
MARK SHANNON
Systems Engineering and Design Integration Group Manager
GIANFRANCO FEDERICI
Head of Department
MATTI COLEMAN
Design Integration and Project Coordination Officer
Plant design integration and modelling
WPMAG project RO
WPRM project RO
EBERHARD DIEGELE
Senior Material Project Control and Integration Officer
Materials and design criteria
WPMAT project RO
SERGIO CIATTAGLIA
Senior Plant Safety Design Integration Officer
Safety design integration
WPSAE project RO
WPBOP project RO
FRANCESCO MAVIGLIA
Plasma Engineering and Analysis Support Officer
Plasma engineering analysis
Engineering data model management
THOMAS FRANKE
Design Integration and Project Coordination Officer
Auxiliary systems design integration
WPHCD project RO
WPDC project RO/ engineering integration
HELMUT HURZLMEIER
Senior CAD operator
CAD management
CAD operations
Project control
System and design integration
Physics integration

## Slide 20: PPPT: allocated by Research Units (EC/k€), 2014-2018
 | Grand Total / EC (k€) | #RUs
Balance of Plant | 1,731 | 4
Breeding Blanket | 24,503 | 7
Containment structures | 861 | n.a.
Diagnostic and control | 1,205 | n.a.
Divertor | 4,753 | 6
Early Neutron Source definition and design | 14,551 | n.a.
H&CD systems | 5,852 | 11
Magnet system | 3,552 | 13
Materials | 29,375 | 22
Plant level system engineering, design integration and physics integration | 7,330 | 14
Remote maintenance system | 7,973 | 7
Safety | 4,291 | 7
Tritium Fuelling and vacuum system | 2,443 | 8
Grand Total | 108,420 | 

## Slide 21: PMU Key Functions
Requirements Analysis
  Stakeholder Requirements Definition / Plant Requirements Analysis
Plant Design Definition and Optimisation
  Plant Design Optimisation Studies
    An Independently moderated TRL Assessment.
    A Parameter trade off assessment and prioritisation exercise.
        Aspect Ratio Scan:
        Development of a blanket attachment system
        Recirculating Electrical Power Requirements
        Sweeping of Divertor Strike Points
    A Critical Decision Making Process
System Level Analysis & Plant Engineering Studies
Systems Engineering Framework and Technical Processes
  Definition of a Systems Engineering Framework
  CAD configuration management
Project Management Activities
  Definition of Deliverables for the CDA
  Formation and Maintenance of the Master Schedule
  Interface Management
DEMO Physics Integration
  System Code Analysis and Development of Point Design Options
  DEMO Physics Basis Development
  DEMO Physics Design Integration
Project Coordination and Control: Scope, Schedule/ Resources
Design and Physics Integration

## Slide 22: Summary
The demonstration of electricity production before 2050 in a DEMO Fusion Power Plant is a priority for the EU fusion program
ITER is the key facility in this strategy and the DEMO design/R&D is expected to benefit largely from the experience gained with ITER construction
Nevertheless, there are still outstanding gaps requiring a vigorous integrated design and technology R&D (e.g., breeding blanket, divertor, materials)
Design integration essential from the early stage to identify requirements for technology and physics R&D
A systems engineering approach is needed to identify design trade-offs and constraints; and prioritize R&D
Ensuring that R&D is focussed on resolving critical uncertainties in a timely manner and that learning from R&D is used to responsively adapt the technology strategy is crucial
Involvement of industry from the early stage is desirable

## Slide 23: EUROfusion Consortium 29 members in 27 EU countries
Thank you for your attention Any Questions?
Acknowledgments
PPPT PMU Team: R. Wenninger, F. Maviglia, M. Shannon, C. Bachmann, B. Meszaros, T. Franke, S. Ciattaglia, E. Diegele, M. Coleman, H. Hurzlmeier, C. Morlock
PPPT Distributed Project Team Leaders: L. Boccaccini (WPBB), J-H You (WPDIV), E. Cipollini (WPBOP), T. Loving (WPRM), L. Zani (WPMAG), M. Rieth (WPMAT), W. Biel (WPDC), M.Q. Tran (WPHCD), C. Day (WPTFV), N. Taylor (WPSAE)
IPH PMU Team: X. Litaudon, D. McDonald
Eurofusion PM: T. Donne
F. Romanelli

## Slide 24: Additional slides

## Slide 25
Divertor: life limiting phenomena is erosion
Armour: Tungsten
HS: Cu-alloys
Coolant: Water
q> 10 MW/m2
Physical sputtering (Te~5 eV) will limit the lifetime of the diveror to 1-2 FPY
Damage in Cu: 3-5dpa/fpy, up to 2 fpy (replacement)
DEMO IVCs lifetime design requirements and materials issues
S. Kecskes (KIT, 2013)
Armour: W
Structural: EUROFER97
Damage in FW steels: 10 dpa/fpy
Starter blanket≈20 dpa; ~6000 cycles.
2nd blanket: 50 dpa
Main Chamber wall/ Breeding Blanket
Advanced Steels
RAFM steels for water-cooled applications
Adv. Steel for High Temperature applications
ODS RAFM steels for high temp strength.
Engineering Data and Design Integration
Materials Database and Handbook
Structural Design Criteria
Testing in fission reactors (HFIR, BOR-60)
IFMIF/ ENS
Material issues
Low-temp. embrittlement of Eurofer (WCLL)
Decline in strength above 550°C
Creep-rupture limits operation to <550°C for >12 103h
Lack of Design-code development
Material issues (Cu-Cr-Zr)
Radiation-induced embrittlement <~200°C
Softening > 350°C
Irradiation data needed