# Task-III Summary

# Dai-Kai Sze      UCSD

# Richard Nygren, SNL

# APEX/TBM Project Meeting

# November 3-5, 2003

# UCLA, Los Angeles, Ca

# Summary

# Status of work

# A molten salt (flinabe) with low melting temperature was identified.

# A self-consistent operating temperature window was established for a liquid wall design, including,

# Large plasma radiation fraction.

# Balanced heat flux distribution on the first wall and the divertor.

# First wall/divertor heat transfer calculations, including the MHD effects.

# Coolant temperature consistent with heat transfer, heat transport.

# Coolant temperature will provide good thermal converting efficiency.

# Large temperature window is available.

# Design configuration and integration, (i.e., piping routes, manifold placements, clearance for remote maintenance) developed with CAD tools.

# Develop nozzle array design layout for coolant supply.

# Neutronics calculations show that sufficient tritium breeding can be achieved for a flinabe blanket.

# Completed safety assessment of blanket and primary coolant loop including the effect of Na and high tritium inventory in the structural material.

# Evaluation of Tritium production, recovery, control, and its impact on safety, was completed.

# Be and Li transmutation was calculated to provide a base for REDOX experiment.

# Divertor design consistent with the reactor parameters, heat flux distribution, and reactor configuration, was completed.

# He pumping was estimated, with consideration of the tritium burn fraction, and D-T throughput.

# Status of papers

# FED Task-III overview paper

# Paper submitted to FED for review

# FED Divertor integration paper

# Paper submitted to FED for review

# SOFE papers

# Liquid Surface Divertor Designs for Fusion Reactors  R. E. Nygren, et al.

# A Fusion Chamber Design with a Liquid First Wall and Divertor, R. E. Nygren, et. al.

# Work needs to be done

# The work on flinabe based APEX activities was a natural stop for the design process.

# The results have been summarized in our reports.

# It will be useful to assess a liquid metal based divertor to determine the power handling capability by a coolant with high thermal conductivity.

# Both Sn and Ga will be interesting candidates.

# Lessons learned

# Flinabe is not only a good selection for a liquid wall coolant, but also can be used for a solid wall design based on FS.

# The temperature window calculation was based on the best calculation we could do now, but had many uncertainties, including

# Plasma edge physics uncertainties.

# Stability of a highly radiative plasma.

# MHD effects on heat transfer, including the effect of wave generation.

# Material properties uncertainties, including the melting temperature of flinabe.

# The temperature limitations between flinabe and FS, including the effects of TF and F2.

# The tritium control in flinabe, and also other breeding materials, will be a serious issue, especially for a high temperature blanket.

# The issue associated with plasma burn fraction, and its impact on He pumping, needs to be carefully assessed.

# The very high heat flux in the divertor can be reduced by a highly radiative plasma. The stability of a highly radiative divertor has to be demontrated.

# The JUPITER-II directed our efforts to REDOX control, and MHD effects on heat transfer. Those are the proper directions for chamber technology R/D.